## Slide 1: EPANET toolkit

## Slide 2: Aim of this lecture
To lean how to use EPANET toolkit to execute an hydraulic simulation

## Slide 3: Problems to solve
Case 1: To satisfy the water demand for Universal Park Beijing, a new pipe line should be placed. What is the most suitable size of this pipe line?
Case 2: After nodal demand allocation from metering data, there is still a 15% gap due to leakage, assuming the leakage is evenly distributed on all pipes, how to allocate these flows easily?

## Slide 4: EPANET toolkit
EPANET is a program that analyzes the hydraulic and water quality behavior of water distribution systems. The EPANET Programmer's Toolkit is a dynamic link library (DLL) of functions that allows developers to customize EPANET's computational engine for their own specific needs. The functions can be incorporated into Windows applications written in C/C++, Delphi Pascal, Visual Basic, or any other language that can call functions within a Windows DLL. The Toolkit DLL file is named EPANET2.DLL and is distributed with EPANET. The Toolkit comes with several different header files, function definition files, and .lib files that simplify the task of interfacing it with C/C++, Delphi, Visual Basic and MATLAB code.
MATLAB
EPANET

## Slide 5: How to run EPANET from MATLAB
Three steps:
  Link MATLAB with EPANET
  Run EPANET functions from MATLAB
  Release the link
Load EPANET library in MATLAB environment
  loadlibrary('epanet2', 'epanet2.h')
Run EPANET functions via CALLLIB function in MATLAB
  [X1,...,XN]=CALLLIB('epanet2','FUNCNAME',ARG1,...,ARGN)
Release link between EPANET and MATLAB
  unloadlibrary('epanet2');

## Slide 6
Exercise 1: to connect EPANET and MATLAB
Use the file provided to practice how to connect EPANET and MATLAB, print on the screen ‘ EPANET library loaded’ and ‘EPANET library released’ to indicate successfully load and unload of library.
Send/share your screenshot

## Slide 7: EPANET toolkit functions
A complete "command line style" simulation
Opening and closing the EPANET Toolkit system
Retrieving information about network nodes
Retrieving information about network links
Retrieving information about time patterns
Retrieving other network information
Setting new values for network parameters
Saving and using hydraulic analysis results files
Running a hydraulic analysis
Running a water quality analysis
Generating an output report

## Slide 8: toolkit functions
Task | Function
Running a complete command line style" simulation | ENepanet
Declaration: int ENepanet( char* f1, char* f2, char* f3, void (*) (vfunc) ) Description: Runs a complete EPANET simulation. Arguments: f1: name of the input file f2: name of an output report file f3: name of an optional binary output file vfunc: pointer to a user-supplied function which accepts a character string as its argument. Returns: Returns an error code.

## Slide 9: toolkit functions
Task | functions
Opening and closing the EPANET Toolkit system | ENopen
 | ENclose
Declaration: int ENopen( char* f1, char* f2, char* f3) Description: Opens the Toolkit to analyze a particular distribution system. Arguments: f1: name of an EPANET Input file f2: name of an output Report file f3: name of an optional binary Output file Notes: ENopen must be called before any of the other toolkit functions (except ENepanet) are used.

## Slide 10: toolkit functions
Declaration: int ENgetnodeindex( char* id, int* index ) Description: Retrieves the index of a node with a specified ID. Arguments: id: node ID label index: node index [errorcode, node_temp] = calllib('epanet2', 'ENgetnodeid', i,node_temp);
Task | Functions
Retrieving information about network nodes | ENgetnodeindex
 | ENgetnodeid
 | ENgetnodetype
 | ENgetnodevalue

## Slide 11: toolkit functions
Declaration: int ENgetlinkindex( char* id, int* index ) Description: Retrieves the index of a link with a specified ID. Arguments: id: link ID label index: link index
Task | Functions
Retrieving information about network links | ENgetlinkindex
 | ENgetlinkid
 | ENgetlinktype
 | ENgetlinkvalue

## Slide 12: toolkit functions
Declaration: int ENgetpatternid( int index, char* id ) Description: Retrieves the ID label of a particular time pattern. Arguments: index: pattern index id: ID label of pattern
Task | Functions
Retrieving information about time patterns | ENgetpatternid
 | ENgetpatternindex
 | ENgetpatternlen
 | ENgetpatternvalue

## Slide 13: toolkit functions
Tasks | functions
Setting new values for network parameters | ENsetcontrol
 | ENsetnodevalue
 | ENsetlinkvalue
 | ENaddpattern
 | ENsetpattern
 | ENsetpatternvalue
 | ENsetqualtype
 | ENsettimeparam
 | ENsetoption

## Slide 14
Declaration: int ENsetnodevalue( int index, int paramcode, float value )
Description: Sets the value of a parameter for a specific node.
Arguments: index: node index paramcode: parameter code (see below) ; value: parameter value
Returns: Returns an error code.
Node parameter codes consist of the following constants: EN_ELEVATION 0 Elevation EN_BASEDEMAND 1 Baseline demand
EN_PATTERN 2 Time pattern index EN_EMITTER 3 Emitter coefficient EN_INITQUAL 4 Initial quality EN_SOURCEQUAL 5 Source quality EN_SOURCEPAT 6 Source pattern EN_SOURCETYPE 7 Source type EN_TANKLEVEL 8 Initial water level in tank

## Slide 15: toolkit functions
Task | functions
Saving and using hydraulic analysis results files | ENsavehydfile
 | ENusehydfile
Declaration: int ENsavehydfile( char* fname ) Description: Saves the current contents of the binary hydraulics file to a file. Arguments: fname: name of the file where the hydraulics results should be saved.

## Slide 16: toolkit functions
Task | Functions
Running a hydraulic analysis | ENsolveH
 | ENopenH
 | ENinitH
 | ENrunH
 | ENnextH
 | ENcloseH

## Slide 17: toolkit functions
Declaration: int ENsolveH( void ) Description: Runs a complete hydraulic simulation with results for all time periods written to the binary Hydraulics file. Returns Returns an error code. Notes: Use ENsolveH to generate a complete hydraulic solution which can stand alone or be used as input to a water quality analysis. It can also be followed by calls to ENsaveH and ENreport to write a report on hydraulic results to the report file. Do not use ENopenH, ENinitH, ENrunH, ENnextH, and ENcloseH in conjunction with ENsolveH. Example: ENopen("net1.inp", "net1.rpt", ""); ENsolveH(); ENsolveQ(); ENreport(); ENclose();

## Slide 18: ENopenH
ENopenH Declaration: int ENopenH( void ) Description: Opens the hydraulics analysis system. Returns: Returns an error code. Notes: Call ENopenH prior to running the first hydraulic analysis using the ENinitH - ENrunH - ENnextH sequence. Multiple analyses can be made before calling ENcloseH to close the hydraulic analysis system. Do not call this function if ENsolveH is being used to run a complete hydraulic analysis.

## Slide 19: ENinitH
Declaration: int ENinitH( int saveflag ) Description: Initializes storage tank levels, link status and settings, and the simulation clock time prior to running a hydraulic analysis. Arguments: saveflag: 0-1 flag indicating if hydraulic results will be saved to the hydraulics file. Returns: Returns an error code. Notes: Call ENinitH prior to running a hydraulic analysis using ENrunH and ENnextH. ENopenH must have been called prior to calling ENinitH. Do not call ENinitH if a complete hydraulic analysis is being made with a call to ENsolveH. Set saveflag to 1 if you will be making a subsequent water quality run, using ENreport to generate a report, or using ENsavehydfile to save the binary hydraulics file.

## Slide 20: ENrunH
Declaration: int ENrunH( long* t ) Description: Runs a single period hydraulic analysis, retrieving the current simulation clock time t. Arguments: t: current simulation clock time in seconds. Returns: Returns an error code. Notes: Use ENrunH along with ENnextH in a do ..while loop to analyze hydraulics in each period of an extended period simulation. This process automatically updates the simulation clock time so treat t as a read-only variable. ENinitH must have been called prior to running the ENrunH - ENnextH loop.

## Slide 21: ENnextH
Declaration: int ENnextH( long* tstep ) Description: Determines the length of time until the next hydraulic event occurs in an extended period simulation. Arguments:
tstep: time (in seconds) until next hydraulic event occurs or 0 if at the end of the simulation period. Returns: Returns an error code. Notes: This function is used in conjunction with ENrunH to perform an extended period hydraulic analysis (see example below). The value of tstep should be treated as a read-only variable. It is automatically computed as the smaller of: ·the time interval until the next hydraulic time step begins ·the time interval until the next reporting time step begins ·the time interval until the next change in demands occurs ·the time interval until a tank becomes full or empty ·the time interval until a control or rule fires

## Slide 22: ENcloseH
ENcloseH Declaration: int ENcloseH( void ) Description: Closes the hydraulic analysis system, freeing all allocated memory. Returns: Returns an error code. Notes: Call ENcloseH after all hydraulics analyses have been made using ENinitH - ENrunH - ENnextH. Do not call this function if ENsolveH is being used.

## Slide 23
Task | Functions
Running a water quality analysis | ENsolveQ
 | ENopenQ
 | ENinitQ
 | ENrunQ
 | ENnextQ
 | ENstepQ
 | ENcloseQ

## Slide 24: ENsolveQ
Declaration: int ENsolveQ( void ) Description: Runs a complete water quality simulation with results at uniform reporting intervals written to EPANET's binary Output file. Returns: Returns an error code. Notes: A hydraulic analysis must have been run and saved to the binary hydraulics file before calling ENsolveQ. It can be followed by a call to ENreport to write a report on hydraulic and water quality results to the report file. Do not use ENopenQ, ENinitQ, ENrunQ, ENnextQ, and ENcloseQ in conjunction with ENsolveQ. Example: ENopen("net1.inp", "net1.rpt", ""); ENsolveH(); ENsolveQ(); ENreport(); ENclose();

## Slide 25: ENnextQ vs. ENstepQ
ENnextQ is used in a do-while loop with ENrunQ to perform an extended period water quality analysis. It allows you to access water quality results at each hydraulic period of the simulation. The water quality routing and reactions are carried out internally at a much smaller time step. Use ENstepQ instead of ENnextQ if you need to access results after each water quality time step.

## Slide 26: toolkit functions
Task | Functions
Generating an output report | ENsaveH
 | ENreport
 | ENsaveinpfile
 | ENresetreport
 | ENsetreport
 | ENsetstatusreport
 | ENgeterror
 | ENwriteline

## Slide 27: Summary:How to Open and Close the Toolkit
The functions for doing this are ENopen and ENclose, respectively.

## Slide 28: Summary:How to Retrieve and Set Network Parameters
The names of retrieval functions all begin with ENget (e.g., ENgetnodevalue, ENgetoption, etc.) while the functions used for setting parameter values begin with ENset (e.g., ENsetnodevalue, ENsetoption, etc.).

## Slide 29: Summary:How to Run a Hydraulic Analysis
There are two ways to use the Toolkit to run a hydraulic analysis: 1.Use the ENsolveH function to run a complete extended period analysis, without having access to intermediate results 2.Use the ENopenH - ENinitH - ENrunH - ENnextH - ENcloseH series of functions to step through the simulation one hydraulic time step at a time. Method 1 is useful if you only want to run a single hydraulic analysis, perhaps to provide input to a water quality analysis. With this method hydraulic results are always saved to the hydraulics file at every time step. Method 2 must be used if you need to access results between time steps or if you wish to run many analyses efficiently. To accomplish the latter, you would make only one call to ENopenH to begin the process, then make successive calls to ENinitH - ENrunH - ENnextH to perform each analysis, and finally call ENcloseH to close down the hydraulics system.

## Slide 30: Summary:How to Run a Water Quality Analysis
Before you can run a water quality analysis, hydraulic results must have been generated either from running a hydraulic analysis or from importing a saved hydraulics file from a previous run. As with a hydraulic analysis, there are two ways to carry out a water quality analysis: 1.Use the ENsolveQ function to run a complete extended period analysis, without having access to intermediate results 2.Use the ENopenQ - ENinitQ - ENrunQ- ENnextQ - ENcloseQ series of functions to step through the simulation one hydraulic time step at a time.

## Slide 31: Summary:How to Retrieve Computed Results
The ENgetnodevalue and ENgetlinkvalue functions are used to retrieve the results of hydraulic and water quality simulations. The computed parameters (and their Toolkit codes) that can be retrieved are as follows:
For Nodes: For Links: EN_DEMAND (demand) EN_FLOW (flow rate) EN_HEAD (hydraulic head) EN_VELOCITY (flow velocity) EN_PRESSURE (pressure) EN_HEADLOSS (headloss) EN_QUALITY (water quality) EN_STATUS (link status) EN_SOURCEMASS EN_SETTING (pump speed etc.)

## Slide 32: Efficiency Issues
When making multiple hydraulic analyses on the same network (as would be done in an optimization procedure), do not use repeated calls to ENsolveH. Instead, use an iterated ENrunH - ENnextH loop!!!!

## Slide 33
Exercise 2: get/set node information
1. Open net 1 file
2. Get pressure of node 22 at 12:00 and 18:00
3. Set nodal demand of node 22 as 1.5 times of the original one, and get pressure of node 22 again.

## Slide 34
Exercise 3: get/set link information
1. Open net 1
2. Get flow of link 21(ID) at 12:00 and 18:00
3. Set diameter of link 21 (ID) as 0.8 times of the original one
4. get and compare nodal pressure of pipe 21 at 12:00 (starting and end nodes) before and after changing of pipe 21’s diameter

## Slide 35
Exercise 4: results presentation
1. Open net 2
2. draw the graph of flow for link 29(ID) for 1 to 72 hours